CEMETERY GROUNDS CARE

For the sake of limiting grounds care costs, all items such as plant stands, solar lights and small memorial items must be affixed onto the stone or its footing, or else have a solid base at least five inches wider than the item on all sides, and must connect or overlap footing of memorial stones base, and be in line with the memorial stone in order to permit mower to continue a straight line with the front and back of the line of stones.

After April 15th and two weeks past Memorial Day, all articles left behind are considered abandoned and may be discarded.

Local management must grant permission for any memorial work to be done in the cemetery. That includes installation of memorials, letter cutting, and monument cleaning.

A Cross or other grave markers of wood, iron, cement, or any like material are prohibited except the standard bronze insignia provided for the graves of veterans or auxiliary members. Enclosures, such as curbs, retaining walls, fences or structures of any kind around lots or graves are not permitted.

When lot owners of adjoining lots, each being designated monument lots, desire to have one memorial placed upon the line between such adjoining lots, both lot owners must sign the foundation permit.

Vases, Urns, Planters, and Other Materials:

The permanent type urn or planter may be used in place of monuments but they must be placed on the conforming line for monuments. They must have a four (4) inch thick foundation, the top of which is flush with the ground and extend five (5) inches from the furthest point of the planter or urn.

The placing of flower boxes, shells, toys, and other miscellaneous items will not be permitted and, if so placed, will be removed by management unless it is affixed to the top of the stone.

Foundation Specifications:

All foundations are to be straight up and down on all sides and the bottom is to be flat. There is to be a four (4) inch collar/apron extending the width and length of the monument.

No post hole auger or other device is to be used to make holes for footings for a monument or marker. The entire area needs to be formed into the foundation.

Pre-cast cement slabs are required to serve as foundations for monuments or markers.

In any section of the cemetery where a memorial is to be placed on an uneven grave, all sides of the top of the foundation are to be level with the ground. There are to be no sharp corners or sudden drop-offs.

Plantings:

The Cemetery Board shall have authority to maintain all trees and shrubs as it sees fit whether these were placed by local management or lot owners. The Cemetery Board/caretaker will remove all floral designs, flowers (natural or artificial), shrubs, plants, or herbage of any kind, from the cemetery grounds as soon as, in their judgment, these plantings and arrangements have become unsightly, dangerous, detrimental, diseased, or do not conform to the regulations.

No bushes, trees or growing plants will be planted in the cemetery without permission of the Cemetery Management. Permanent potted plants, flower vases or other growing decoration must be placed either on the upright memorial or along side on the monument line. No decoration will be permitted that would interfere with mowing and trimming of the cemetery.

Artificial Floral Arrangements and Other Materials:

No bouquets or artificial arrangements are to be staked into the grave area except as noted above.

Local management will not be liable for floral pieces, baskets, misplaced or broken flower vases, or flag standards.